## Slide 1: Longitudinal Tunnel Ventilation and the Fire Throttling Effect
Edmund Ang
Hazelab @ Imperial College London
AECOM @ Fire & Risk
June, 2017

## Slide 2: Contents
A brief introduction to tunnel ventilation, super critical ventilation velocity and how it relates to the fire throttling effect.
Tunnel Ventilation: An Overview
Tunnel Ventilation: Longitudinal System
Critical and Super Critical Ventilation Velocity
Fire Throttling Effect
Conclusion

## Slide 3: Society of Fire Safety Research Grant 2017
Acknowledgement
“If I have seen further, it is by standing on the shoulders of giants”
Isaac Newton

## Slide 4: Hazelab @ Imperial College London
Our work is to reduce the worldwide burden of accidental fires and protect people, their property, and the environment.
Research Group headed by Guillermo Rein
13 PhD researchers
1 Postdoc
Research in:
  Forest fires
  Built Environment
  Material Flammability

## Slide 5: Tunnel Ventilation An Overview

## Slide 6: Tunnel Ventilation: An Overview
Purpose of ventilation
Temperature
  Cooling
  Auxiliary equipment
Air Quality
  CO and fumes
  Oxygen starvation (petrol / diesel)
Fire emergencies

## Slide 7: Tunnel Ventilation: An Overview
Ventilation systems
  Natural / Passive
  Mechanical / Active
Natural / Passive
  Piston effect
  Wind
  Chimney Effect
Piston Effect
Chimney Effect

## Slide 8: Tunnel Ventilation: An Overview
Ventilation systems
  Natural / Passive
  Mechanical / Active
Mechanical / Active
  Transverse
  Semi-transverse
  Longitudinal
Roads and Maritime Services. TP04 Road Tunnel ventilation system, July 2014

## Slide 9: Tunnel Ventilation Longitudinal Ventilation

## Slide 10: Tunnel Ventilation: Longitudinal Ventilation
Longitudinal ventilation
  Air flow in one direction
  Single direction traffic
  Not viable previously; need for large quantities of fresh air
  Used for the majority of tunnels in Australia last 20 years
  Easier to construct than transverse systems

## Slide 11: Tunnel Ventilation: Longitudinal Ventilation
Longitudinal ventilation in fire mode
  Keep one side clear of the fire / smoke for evacuation
  Air flow > critical ventilation velocity, Vc

## Slide 12: Tunnel Ventilation: Longitudinal Ventilation
Longitudinal ventilation in fire mode
  Keep one side clear of the fire / smoke for evacuation
  Air flow > critical ventilation velocity, Vc
Backlayer: Air flow < Vc
No backlayer: Air flow > Vc
D. Swenson. Critical velocity in tunnel fires.
Thunderhead Engineering.

## Slide 13: Tunnel Ventilation Critical Ventilation Velocity

## Slide 14: Tunnel Ventilation: Critical Ventilation Velocity
Velocity needed to prevent backlayering of smoke
One of the most studied phenomenon
1950s: Origins traced back to Thomas (Fire Research Station, UK)
  Argued critical velocity governed by the ratio of buoyancy to inertial forces
  Relationship linked by Froude Number
1970s: Refinements by Heselden
1980s: Refinements by Danziger and Kennedy
  Related temperature to convective heat release rate
  Cornerstone of tunnel ventilation design

## Slide 15: Tunnel Ventilation: Super Critical Ventilation Velocity
1995: Oka and Atkinson defined ‘super critical’ ventilation velocity
So what is the super critical ventilation velocity?
Fire size and critical velocity
  Relationship up to a limit
  No increase in velocity needed beyond
  Typically ~ 3 to 4 m/s for road tunnels
A. Vaitkevicious and R. Carvel. Investigating the throttling effect in tunnel fires.
Fire Technology, June 2015

## Slide 16: Tunnel Ventilation: Super Critical Ventilation Velocity
2000: Further refinements by Wu and Bakar
Further experiments showing this
Foundation of other researches
  Tunnel dimensions
  Relationship between velocity and fire growth
  Slope in tunnels
  Blockages in tunnels
  Critical velocity near portals
Modified equation used today
  NFPA 502 etc
C.C. Hwang and J.C. Edwards. The critical ventilation in tunnel fires .
Fire Safety Journal, 2002.

## Slide 17: Fire Throttling Effect So how does it all relate?

## Slide 18: Tunnel Ventilation: Fire Throttling Effect
So what is the fire throttling effect?
An observed phenomenon where a fire increases the flow resistance
Pressure drop / flow resistance due to fires
A. Vaitkevicious and R. Carvel.
Investigating the throttling effect in tunnel fires.
Fire Technology, June 2015

## Slide 19: Tunnel Ventilation: Fire Throttling Effect
1973: First discussed for mining tunnels by Greuer
1979: Experimental observations by Lee
A forgotten and overlooked period
2014: Rediscovered by Colella et al whilst working on the novel multi-scale modelling approach for long tunnels
PIARC Jet Fan Calculation Procedure
  A recognised phenomenon
  To be verified in a CFD study

## Slide 20: Tunnel Ventilation: Fire Throttling Effect
The impact of the fire throttling effect has been observed
No analytical or empirical model describing this
But a numerical glimpse in the FDS Multi-scale fire modelling work
Dartford Tunnel in London
F. Collela, R. Borchiellini, V. Verda, and G. Rein.
Multiscale Modelling of Tunnel Ventilation Flows and Fires.
[Online] https://www.era.lib.ed.ac.uk/handle/ 1842/3528, May 2010.
C.D.E. Ang, G. Rein, J. Peiro and R. Harrison
Simulating longitudinal ventilation flows in long tunnels CFD and Multi-scale modelling
Tunnellling and Underground Space Technology, February 2016

## Slide 21: Tunnel Ventilation: Fire Throttling Effect
Reduction in mass flow

## Slide 22: Tunnel Ventilation: Fire Throttling Effect
Jet fans
Jet fans
Cold flow pressure
Throttling effect?

## Slide 23: Conclusion
Longitudinal tunnel ventilation will continue to be a popular means to ventilate a tunnel
Fire throttling effect is an important consideration
For a larger fire, the number of fans needed to achieve the critical velocity increases (the critical velocity remains unchanged)
We do not have an analytical or empirical description of this yet
Only through ‘black box’ CFD modelling – how accurate?
We are working on this – My PhD research!

## Slide 24: Thank You
edmund.ang@aecom.com
chin.ang13@imperial.ac.uk
June, 2017